## Slide 1: Use Cases of GIP6
Cong Li ,China Telecom
2023.3.28

## Slide 2: Enterprise site to the DC
        Backbone Network
Metropolitan-area Network
        Backbone Network
Enterprise site
DC
Cloud desktop
Media storage
Computing
CDN+
Managent
SR/DCSW
Management SW
Could Network POP
User Reqirement：
Small and Medium-sized enterprises： services and data in public cloud
Some Typical applications（AR/VR）：Strict QoS requirements, Delay-sensitive
Current Network Solution：
Enterprise sites can be connected to cloud network POP through SRv6 tunnels.
Vxlan tunnels are used to connect the Spine nodes and Leaf nodes or multiple leaf nodes in data centers.
Problem：
        IFIT technology is used in MAN and backbone network
However, end-to-end quality monitoring of the specified path cannot be implemented based on Vxlan tunnels in the data center. It is difficult to accurately locate faults in DC.
Campus Network
PE
SRv6 tunnel
SRv6 tunnel
VxLANl
Notes: Small and Medium-sized enterprises are most likely to deploy their services and data in public cloud and continue to using this as their main service mode in the future .
Some Typical applications such as AR/VR are delay-sensitive，and the delay must be less than 20ms
To meet the requirements of enterprises, operators need to provide connections from the enterprise site to DC quickly and agilely.
Srv6 has been widely deployed in metropolitan area networks and backbone networks.
Point-of-Presence
However, end-to-end quality monitoring of the specified path cannot be implemented based on Vxlan tunnels in the data center.

## Slide 3: Interconnection between DCs
Backbone Network
Corporate headquarters
Site 1
Site 2
Site 3
Site 4
DC2
Cloud desktop
Media storage
Computing
CDN+
Managent
SR/DCSW
Management SW
Could Network POP
DC1
Cloud desktop
Media storage
Computing
CDN+
Managent
SR/DCSW
Management SW
Could Network POP
User Reqirement：
Large-scale enterprise：Interconnection between enterprise sites and collaboration of DCs
Some Typical applications（scientific calculation）： Bandwidth, delay, packet loss rate and jitter.
Current Network Solution：
Data centers are interconnected through VxLAN and SRv6 tunnels
Problem：
In addition to problem of locating faults in the data center, some data in this scenario needs to be transmitted securely.
VxLAN tunnel requires to realize some emerging and useful functionalities （iFIT, security）.
Notes: Large-sized enterprises require interconnection of multiple sites and collaboration between different data centers.
In a scientific computing scenario,The data of each branch needs to be sent back to the headquarters, and the amount of original data reaches TB size, which requires large network bandwidth. In addtion.Due to the timeliness of the calculation results, the service has strict requirements on network delay, packet loss rate, and jitter.
In addition, the interconnection of multiple data centers is necessary to collaborate to complete complex computing tasks.
However，VXLAN does not have transmission security fuction。
in conclusion，VxLAN tunnel requires to realize some emerging and useful functionalities （iFIT, security）.In this way, VxLAN can better cooperate with Srv6 technology to ensure the quality of service end-to-end.

## Slide 4: Thank you!