## Slide 1: GIP6 Problem Statement
China Unicom
March 2023
研院 未来网络研究部

## Slide 2: Current status of IP tunnels
Existing IP tunnels:
IP Tunnel Type | Defined Doc
GRE | RFC2784
IP in IP | RFC1853
L2TPv3 | RFC3931
ISATAP | RFC4214
IPv4/IPv6 over IPv6 (4 over 6) | RFC2473
VXLAN | RFC7348
NVGRE | RFC7637
MPLS over UDP | RFC7510
VXLAN-GPE (Generic Protocol Extension for VXLAN) | I-D.ietf-nvo3-vxlan-gpe
New feature encapsulation over IPv6:
Feature | Defined Doc
IPv6 encaps for Alternate Marking | I-D.ietf-6man-ipv6-alt-mark
IPv6 encaps for IOAM | I-D.ietf-ippm-ioam-ipv6-options
IPv6 encaps for determing resource isolation | I-D.dong-6man-enhanced-vpn-vtn-id
IPv6 encaps for an APN | I-D.li-apn-ipv6-encap

## Slide 3: Issues on new feature extention (1/2)
Issues when support new features based on existing IP tunnels:
Lots of standardization work for extending all the IP tunnels .
IPv6 can directly support some functions of these IP tunnels which cannot be done over the IPv4, which makes such functions become redundant over the IPv6.
Some IP tunnels have their own headers.
  Option 1: Reusing the exiting IPv6 encapsulations based on the IPv6 extension header
  Option 2: Define new extensions based on their own tunnel headers

## Slide 4: Issues on new feature extention (2/2)
MPLS is also doing some related work，is there any overlap?
Even if the GIP6 solution is adopted, there is still lots of work to do, can we make it?
MPLS:
  When packets enter MPLS tunnels from IPv6 domain, info encapsulated in IPv6 header will be lost, which prevents cross-domain fine-grained OAM/PM;
GRE:
  Repetitive implementation of functionalities that is already done in IPv6
  GRE header lacks of scalability to encapsulate more information.
VxLAN:
  Lots of standardization and repetitive development work if implement new functionalities in underlay network
  Underlay functionalities are encapsulated in overlay layer header

## Slide 5: Thanks